North Dakota and Minnesota state law as well as Fargo & Moorhead City Ordinances require any facility offering parking for employees or visitors to provide accessible parking for individuals with disabilities.

Is MY business required to comply with accessible parking requirements? YES! If you own, operate, or lease a business that serves the public, you are required to comply with the Americans with Disabilities Act (ADA) which mandates the removal of “physical barriers” that are “readily achievable.”  This includes having proper accessible parking signage and parking lot striping.

DEFINITION

An accessible parking space consists of a vehicle space with proper signage, and a striped access aisle.   The entire space must be kept clear of obstructions at all times, including ice, snow, shopping carts, trash cans, potted racks, seasonal garden displays, bicycle racks, etc.

LOCATION AND ROUTE

Accessible parking spaces must be located on the shortest accessible route of travel to an accessible facility entrance.  Where buildings have multiple accessible entrances with adjacent parking, the accessible parking spaces must be dispersed and located closest to the accessible entrances.  An accessible route never has curbs or stairs, must be at least 5 feet wide, and has a firm, stable, slip-resistant surface.  The slope along the accessible route should not be greater than 1:12 in the direction of travel.

How can my business comply with accessible parking requirements?

The following Chamber-member sign companies are ready to help with your accessible parking signage needs, most offering up to a 10% discount if you can identify yourself as a Chamber-member business and mention this letter!

Cook Sign Co…………….	235-5323			FRS Industries……………235-5347

Fast Signs……..............	365-8300			Indigo Signworks.........297-9696

Sign Pro…………………….461-7309			Mathison’s Express Press Graphics……….232-8971

Sign *A* Rama………….478-7900			Custom Graphics Signs & Design…………..237-5685

FedEx Kinko’s…………….235-3411			3D Specialties…………….293-8599

PARKING LOT STRIPING

When a business re-stripes a parking lot, it must provide accessible parking spaces as required by the ADA Standards for Accessible Design. In addition, businesses or privately-owned facilities that provide goods or services to the public have a continuing ADA obligation to remove barriers to access in existing parking lots when it is readily achievable to do so.  In the state of North Dakota, accessible parking spaces must be designated with blue paint.

SIZE

Standard accessible parking spaces must be a minimum of 8 feet wide with a minimum 5-foot wide aisle adjacent to it.  Van parking spaces shall be permitted to be 8 feet minimum in width only if the adjacent aisle is increased to 8 feet as well; otherwise van accessible parking spaces must be kept at a minimum 11-foot wide, adjacent to the standard 5-foot aisle to maintain a total width of 16 feet.  (See Figure A above for clarification)

| HOW TO CALCULATE YOUR TOTAL REQUIRED ACCESSIBLE PARKING |
| --- |
| Amount of Regular Parking Provided in Facility’s Lot | Standard Accessible Parking Spaces | Van Accessible Parking Spaces | Minimum Required Accessible Parking Spaces |
| 1 to 25 | 0 | 1 | 1 |
| 26 to 50 | 1 | 1 | 2 |
| 51 to 75 | 2 | 1 | 3 |
| 76 to 100 | 3 | 1 | 4 |
| 100 to 150 | 4 | 1 | 5 |
| 151 to 200 | 5 | 1 | 6 |
| 201 to 300 | 5 | 2 | 7 |
| 301 to 400 | 6 | 2 | 8 |
| 401 to 500 | 7 | 2 | 9 |
| 501 to 1000 |  | 1 per 6 accessible | 2% of total reg. parking |
| 1001 and over |  | 1 per 6 accessible | 20 plus 1 for each 100 over 1000 |

APPROPRIATE SIGNAGE

Section 8-1003(K) of the Fargo City Municipal Code regulates parking in spaces designated for mobility-impaired persons.  Unauthorized parking in a space designated for mobility-impaired persons carries a $100 fee.

An entity that fails to comply with signage and pavement markings is guilty of an infraction ($500 fine) if the entity does not correct such violations within sixty (60) days after receiving official notice thereof.  Fargo’s ordinance follows state law.  See N.D.C.C. 39-01-15(9), 39-01-15(10), and 39-01-15(12).

SIGN DETAILS

The bottom of the lowest sign shall be a minimum of 5 feet above the pavement.  Signs may be mounted higher for better visibility.  Standard and van-accessible parking space signs must state, “RESERVED PARKING” and include the Universal Symbol of Accessibility.

Supplemental signage must state, “UNAUTHORIZED PARKING MANDATES $100 FEE”.  A van-accessible parking space requires an additional sign stating, “VAN ACCESSIBLE”.

# Text boxes

Figure A

Car Parking Diagram (left)

and Van Parking Diagram

(right).

Figure B

Accessible Parking Signage